## Slide 1: Which buildings waste the most energy?
MATLAB HACKATHON 2026 · TEAM CCEB ANATA
Predicting Site Energy Use Intensity for 9,705 buildings, using MATLAB and Regression Learner models
Duong Minh Triet · Nguyen Dang Quang · Huynh Xuan Lam · Vuu Tan Loc
Notes: Hi, we’re team CCEB ANATA. Buildings are a big share of energy use and emissions. If we can predict how much energy a building should use, we can spot the ones using far more than expected. Those are the best candidates for retrofitting. In five minutes we’ll show how we cut the prediction error step by step, starting from a naive guess.

## Slide 2: The task: predict energy use per square foot
75,757
building-years to learn from, across 6 years and 7 anonymised US states
9,705
buildings to predict, all from the following year
60
facility types, from offices and schools to data centres and hospitals
Inputs: building facts (floor area, year built, Energy Star rating) and local weather. Target: Site EUI, scored by RMSE.
Notes: Each row is one building in one year. We get building characteristics and the weather where it stands, and we predict Site Energy Use Intensity: energy per square foot per year. The score is root mean squared error, roughly the typical size of a miss in EUI units.

## Slide 3: Exploring the data: the test set is not like training
What we found | What we did about it
Test is one future year (year 7) | Validate on the latest year, not a random split
State 6 is 67% of training, 0% of test | Score a “test-like” subset without State 6
Wind and fog columns 88–94% empty in test | Dropped them
Energy Star rating missing for ~1 in 3 | Kept it, plus a “missing” flag
Year built recorded as 0 for some buildings | Treated as missing
Notes: Before modelling we compared train and test. The test set is a future year, and one state that dominates training doesn’t appear in test at all. Several weather columns are almost empty in test. Each finding drove a specific cleaning or validation decision, shown on the right.

## Slide 4: Validation that mimics the real test
Years 1–5
Train
Year 6
Validate
Year 7
Hidden test
+4.2
RMSE points worse on the test-like buildings (no State 6) than on all of year 6. A random split would have hidden this gap, so every model choice used the test-like score.
Notes: A random 80/20 split mixes years, so the model gets to peek at the same buildings in the same year. Instead we train on years 1 to 5 and validate on year 6. We also score only buildings outside State 6, because the test set has none. For the random forest, that test-like score was 47.0 against 42.8 on all of year 6, a 4.2 point gap we would have missed otherwise. After choosing the model, we retrain on all six years.

## Slide 5: In the code: a time-based split
% Test is a future year, so a random split would be too optimistic.
% Train on years 1-5 and validate on year 6.
isVal = train.Year_Factor == 6;
trainSet = train(~isVal, :);
valSet = train(isVal, :);
% Test has no State_6, so also score a "test-like" subset
valTestLike = valSet.State_Factor ~= "State_6";
From step1_prepare_data.m. Every model is scored on valTestLike, the rows that look most like the hidden test set.

## Slide 6: Features with a physical reason behind them
Log floor area
Sizes span several orders of magnitude
Seasonal temperatures
36 monthly columns summarised as winter, summer and annual range
Missing rating flag
Unrated buildings behave differently from rated ones
No year index
Year 7 is outside the training range, so the model must not lean on it
Notes: Every feature has a reason. Floor area is log-scaled. The 36 monthly temperatures become three seasonal summaries. A missing Energy Star rating is treated as information. And we left out the year index on purpose, because the test year lies outside anything the model has seen.

## Slide 7: The same buildings come back every year
THE BREAKTHROUGH
There is no building ID, but state + class + facility type + floor area + year built identifies a building. 93% of test buildings match one we have seen before, so last year’s energy use becomes a feature.
Lag features: last known EUI, mean past EUI, years of history, years since last seen
Notes: This was the key idea, and it’s also what the top WiDS 2022 teams relied on. The data hides building IDs, but a combination of five fixed attributes is almost unique per building. Matching on it, 93 percent of test buildings have history. A building’s own past energy use is a far better guide than any weather variable.

## Slide 8: In the code: rebuilding building IDs and their history
% No building ID: rebuild one from the 5 columns that never change
keyVars = ["State_Factor", "building_class", "facility_type", "floor_area", "year_built"];
bld = findgroups(both.State_Factor, both.building_class, both.facility_type, ...
both.floor_area, yearBuilt);
for y = unique(yr)'
past = byYear(byYear.yr < y, :); % only EARLIER years: no peeking
if isempty(past), continue; end
[pastBld, lastIdx] = unique(past.bld, "last");
stats = groupsummary(past, "bld", "mean", "mean_eui");
[isKnown, loc] = ismember(bld, pastBld);
rows = yr == y & isKnown;
lagLast(rows) = past.mean_eui(lastIdx(loc(rows))); % last known EUI
lagGap(rows) = y - past.yr(lastIdx(loc(rows))); % years since seen
lagMean(rows) = stats.mean_mean_eui(loc(rows)); % average past EUI
lagCount(rows) = stats.GroupCount(loc(rows)); % years of history
end
From step1_prepare_data.m (excerpt). Year 6 validation sees only years 1–5; test year 7 gets history from years 1–6.

## Slide 9: Each iteration cut the error
Predict the average
64.9
Linear Regression
54.3
Boosted Trees, tuned
48.5
Bagged Trees (random forest)
47.0
Average of both ensembles
46.8
Bagged Trees + lag features
26.4
RMSE on test-like validation (year 6, excluding State 6). Lower is better. All models are Regression Learner presets.
Notes: Here’s the iteration story. Predicting the average gives 64.9. Linear regression gets to 54.3. Tree ensembles do better: boosted trees 48.5, bagged trees 47.0, and averaging the two gives 46.8 because they make different mistakes. Then the building-history features bring bagged trees down to 26.4, almost halving the error again. Even linear regression drops from 54.3 to 35.8 with them. Every model here is available in MATLAB’s Regression Learner app.

## Slide 10: In the code: let the evidence pick the model
% Averaging two different tree ensembles often cancels part of their errors
results = addResult(results, "Average of forest and boosting", ...
(yhatRF + yhatBest) / 2);
candidates = ["Random forest", "Boosted trees, tuned", ...
"Average of forest and boosting"];
candRows = find(ismember(results.Model, candidates));
[~, k] = min(results.RMSE_TestLike(candRows));
finalChoice = results.Model(candRows(k));
From step2_train_models.m. Step 3 retrains finalChoice on all six years before predicting the test set.

## Slide 11: A MATLAB lesson: how trees handle missing values
The problem
Without surrogate splits, a building with a missing value stops partway down each tree and gets a rough average. About 1 in 3 buildings has no Energy Star rating.
Our fix
Replace missing values with an out-of-range marker (−999) for tree models only, so they get their own branch. The “missing” flag keeps the information.
Notes: We noticed our MATLAB trees scored well below the same features in another library. The reason is how fitrensemble trees treat NaN at prediction time. Filling missing values with a sentinel value outside the normal range lets the trees route those buildings down their own branch. The linear model still uses median imputation.

## Slide 12: In the code: giving missing values their own branch
function X = fillSentinel(X)
% Replace NaN in numeric predictors with an out-of-range value for tree models.
% MATLAB trees without surrogate splits stop a NaN observation at the split node,
% so an explicit sentinel lets the tree send "missing" down its own branch.
isNum = varfun(@isnumeric, X, "OutputFormat", "uniform");
for v = string(X.Properties.VariableNames(isNum))
X.(v) = fillmissing(X.(v), "constant", -999);
end
end
fillSentinel.m, applied before every tree model. Linear regression keeps median imputation instead.

## Slide 13: One command reproduces everything
1 · Prepare
Clean, engineer features, build year-based split
2 · Compare
Train baselines and ensembles, tune, pick the best automatically
3 · Submit
Retrain on all years, predict, check against sample format
>> runAll
Code: github.com/dgmtriet/Hackathon2026 · branch lam_workings
Notes: The whole solution is three scripts and a few helper functions. runAll runs them end to end with no manual steps, fixed random seeds, and asserts that the submission matches the sample file’s format. The code is public on GitHub.

## Slide 14: What we’d tell the next team
Look at how the test set differs before choosing a split
Domain knowledge beat model choice: a building’s past use is its best predictor
Know how your tools treat missing values
Simple app models, used carefully, go a long way
Next: rank buildings by how far they exceed their predicted EUI to target retrofits.
Notes: Four takeaways. Check the test set first. Domain thinking, like recognising that buildings repeat over years, mattered more than which algorithm we picked. Understand your tools. And standard Regression Learner models were enough. The natural next step is to use the model the way it was meant to be used: flag buildings that use far more energy than predicted, as retrofit candidates. Thank you.