## Slide 1: Predicting Building Energy Use Intensity
MATLAB HACKATHON 2026 · CCEB ANATA · 30 OCTOBER 2026
A validated MATLAB pipeline that predicts Site EUI for 9,705 buildings with a test-like RMSE of 25.99
Duong Minh Triet · Nguyen Dang Quang · Huynh Xuan Lam · Vuu Tan Loc
Notes: Good morning. We’re team CCEB ANATA. Our task was to predict how much energy a building uses per square foot per year, its Site Energy Use Intensity, from its characteristics and local weather. Accurate predictions matter because buildings that use far more energy than predicted are the best candidates for retrofits. Over the next few minutes we’ll walk through how we audited the data, designed a validation that matches the real test, engineered features, compared models, and ended with a test-like RMSE of 25.99, down from 64.88 for a naive baseline.

## Slide 2: Agenda
OVERVIEW
# | Section | Key question
1 | Task and data audit | What are we predicting, and how does test differ from train?
2 | Cleaning and validation | How do we measure progress honestly?
3 | Feature engineering | Which inputs carry the signal?
4 | Models and results | Which Regression Learner model wins, and by how much?
5 | Submission and conclusions | What did we deliver and learn?
Overview · 2 / 20
Notes: Here’s our structure. We start with the task and an audit of the data, because what we found there shaped every later decision. Then we cover how we cleaned the data and designed a validation that mirrors the hidden test set. Next comes feature engineering, including the building-history features that made the biggest difference. Then the models and results, all using models from MATLAB’s Regression Learner app. We finish with the submission and our conclusions.

## Slide 3: Predict Site EUI for each building in a future year
1 · TASK
TARGET
Site EUI
Energy used per square foot per year (kBtu/ft²), from utility bills
INPUTS
62 columns
Building facts (type, floor area, year built, Energy Star rating) and local weather
METRIC
RMSE
Root mean squared error, in EUI units. Lower is better; large misses weigh most.
Why it matters: buildings that use far more energy than their prediction are the strongest retrofit candidates.
Data: WiDS Datathon 2022 · Task and data audit · 3 / 20
Notes: The target is Site EUI, the energy a building uses per square foot per year, measured from utility bills. Each row has 63 input columns: building facts such as facility type, floor area, year built and Energy Star rating, plus weather at the building’s location. Predictions are scored by RMSE, root mean squared error, which is in the same units as EUI. Because errors are squared, a few large misses dominate the score. The practical use is retrofit targeting: if a building uses much more than predicted, it’s probably wasting energy.

## Slide 4: 75,757 training rows over six years; test is year 7
1 · DATA AUDIT
Year | Rows | Share
1 | 2,117 | 2.8%
2 | 9,058 | 12.0%
3 | 10,879 | 14.4%
4 | 12,946 | 17.1%
5 | 18,308 | 24.2%
6 | 22,449 | 29.6%
7 (test) | 9,705 | —
Each row is one building in one year.
7 anonymised states, 2 building classes, 60 facility types.
Recent years dominate: year 6 alone is 29.6% of training data.
Source: train.csv, test.csv · Task and data audit · 4 / 20
Notes: The training data has 75,757 rows spread over six anonymised years, and the number of rows grows each year, so year 6 alone is almost 30 percent. The test set is 9,705 rows, all from year 7. Each row is one building in one year, across seven anonymised states, two building classes and sixty facility types. The key point is that we’re predicting a future year, which immediately tells us a random train-test split won’t reflect the real task.

## Slide 5: The target is strongly right-skewed
1 · DATA AUDIT
Site EUI statistic | Value
Mean | 82.6
Standard deviation | 58.3
Minimum | 1.0
25th percentile | 54.5
Median | 75.3
75th percentile | 97.3
Maximum | 997.9
356
training rows above 400, more than 5× the median
4.7
skewness. A few extreme buildings dominate RMSE.
Source: train.csv, n = 75,757 · Task and data audit · 5 / 20
Notes: Here’s the target in numbers. The median building uses about 75 kBtu per square foot per year, but the distribution has a long right tail. The maximum is almost 1,000, 356 training rows are above 400, and the skewness is 4.7. That matters for two reasons. First, RMSE squares errors, so these rare extreme buildings carry a lot of weight in the score. Second, it suggested trying a log-transformed target, which we tested and report later.

## Slide 6: The test set comes from a different mix of states
1 · DATA AUDIT
State | Train share | Test share
State 6 | 67.1% | 0.0%
State 11 | 8.5% | 33.7%
State 4 | 5.7% | 26.5%
State 2 | 6.4% | 15.6%
State 8 | 4.9% | 13.6%
State 1 | 7.4% | 10.6%
State 10 | <0.1% | <0.1%
Two-thirds of training rows come from a state the model will never be tested on.
Building class also flips: residential is 57.5% of train but 42.2% of test.
Source: train.csv, test.csv · Task and data audit · 6 / 20
Notes: This was the most important finding of the audit. State 6 makes up 67 percent of the training data and zero percent of the test data. The test set is dominated by States 11 and 4 instead. The building mix shifts too: residential buildings are 57.5 percent of training but only 42 percent of test. So a model that scores well on all of the training data could be scoring well mostly on State 6, which doesn’t matter for the test. We designed our validation around this.

## Slide 7: Six columns have gaps, four are nearly empty in test
1 · DATA AUDIT
Column | Missing, train | Missing, test | Decision
days_with_fog | 60.5% | 93.9% | Drop
direction_peak_wind_speed | 55.2% | 88.4% | Drop
direction_max_wind_speed | 54.2% | 88.4% | Drop
max_wind_speed | 54.2% | 88.4% | Drop
energy_star_rating | 35.3% | 23.2% | Keep, add a missing flag
year_built | 2.4% | 0.9% | Keep; treat 0 as missing
All other input columns are complete. Six training rows record year_built as 0.
Source: train.csv, test.csv · Task and data audit · 7 / 20
Notes: Six columns have missing values. The four wind and fog columns are more than half empty in training and close to 90 percent empty in test, so even a perfect relationship couldn’t be used at prediction time. We dropped them. Energy Star rating is missing for about a third of training rows, but it’s a strong signal when present, so we kept it and added a flag for whether it’s missing. Year built has a few gaps plus six rows recorded as zero, which we treat as missing.

## Slide 8: Every cleaning step traces back to an audit finding
2 · CLEANING
Step | Reason
Drop 4 wind and fog columns | 88–94% missing in test
Drop Year_Factor as a predictor | Test year 7 lies outside the training range
year_built = 0 → missing | Placeholder, not a real year
Add energy_star_missing flag | Unrated buildings behave differently from rated ones
Add log_floor_area | Floor area spans several orders of magnitude
Add winter, summer and range temperatures | Summarise 36 correlated monthly columns
Shared categories for text columns | Train and test encode states and types identically
Code: step1_prepare_data.m, cleanFeatures() · Cleaning and validation · 8 / 20
Notes: Every cleaning step is tied to something we saw in the audit. We drop the four wind and fog columns and the year index. A year built of zero becomes missing. A missing Energy Star rating gets its own flag. Floor area is log-scaled because it spans several orders of magnitude, and the 36 monthly temperature columns are summarised into winter, summer and annual range. Finally, the text columns are converted to categoricals with the same categories in train and test, so a state or facility type means the same thing in both. The same cleaning function runs on train and test.

## Slide 9: A time-based split scored on test-like buildings
2 · VALIDATION
Train · years 1–5
53,308 rows
Validate · year 6
22,449 rows
Test · year 7
9,705 rows
Test-like subset
Year 6 without State 6: 9,432 rows. Every model decision uses this score.
Why it matters
First random forest: 42.8 on all of year 6 vs 47.0 test-like, a 4.2 point gap.
After model selection, the final model is retrained on all six years · Cleaning and validation · 9 / 20
Notes: Because the test is a future year, we hold out the most recent year instead of a random sample. We train on years 1 to 5, 53,308 rows, and validate on year 6, 22,449 rows. Because the test set has no State 6, we also compute a test-like score on the 9,432 year-6 rows outside State 6, and every model decision uses that score. It matters: our first random forest scored 42.8 on all of year 6 but 47.0 on the test-like rows. A random split would have hidden that gap. Once the model is chosen, we retrain on all six years before predicting the test set.

## Slide 10: The final models use 66 predictors
3 · FEATURES
Group | Count | Columns
Building and location | 7 | State, class, facility type, floor area, year built, Energy Star rating, elevation
Monthly temperatures | 36 | Min, average and max for each month
Annual weather | 14 | Degree days, precipitation, snow, average temperature, days above or below thresholds
Engineered | 5 | energy_star_missing, log_floor_area, winter, summer and range temperatures
Building history | 4 | lag_last, lag_mean, lag_count, lag_gap
Total | 66 | Excluded: id, site_eui, Year_Factor, 4 wind and fog columns
Source: predictorNames in preparedData.mat · Feature engineering · 10 / 20
Notes: This is the complete feature set. 57 original columns survive cleaning: seven building and location columns, 36 monthly temperatures and 14 annual weather measures. We add five engineered features and four building-history features, for 66 predictors in total. Excluded are the row id, the target itself, the year index, and the four wind and fog columns. The four history features in the highlighted row are the subject of the next slide, and they turned out to be the most important part of the model.

## Slide 11: The same buildings reappear every year
3 · KEY INSIGHT
There is no building ID, but five attributes never change for a building:
State · building class · facility type · floor area · year built
Matching on this key gives each row the building’s Site EUI from strictly earlier years only.
93.4%
of test buildings match a building seen in training
Feature | Definition
lag_last | Site EUI in the most recent earlier year
lag_mean | Average Site EUI over all earlier years
lag_count | Number of earlier years observed
lag_gap | Years since the building was last observed
Same core idea as the WiDS 2022 top solutions · Feature engineering · 11 / 20
Notes: This is the insight that changed our results. The data has no building ID, but the same buildings come back year after year. State, building class, facility type, floor area and year built never change for a given building, so together they act as an ID. 93.4 percent of test buildings match a building we’ve seen in training. For every row we then look up that building’s energy use in strictly earlier years and create four features: the last known EUI, the average past EUI, how many years of history exist, and how long since it was last seen. Using only earlier years means the model never sees the future, so the validation stays honest. This is the same core idea the top WiDS 2022 teams used.

## Slide 12: Building history in MATLAB
3 · IMPLEMENTATION
bld = findgroups(both.State_Factor, both.building_class, both.facility_type, ...
both.floor_area, yearBuilt); % rebuilt building ID
for y = unique(yr)'
past = byYear(byYear.yr < y, :); % earlier years only
if isempty(past), continue; end
[pastBld, lastIdx] = unique(past.bld, "last");
stats = groupsummary(past, "bld", "mean", "mean_eui");
[isKnown, loc] = ismember(bld, pastBld);
rows = yr == y & isKnown;
lagLast(rows) = past.mean_eui(lastIdx(loc(rows)));
lagGap(rows) = y - past.yr(lastIdx(loc(rows)));
lagMean(rows) = stats.mean_mean_eui(loc(rows));
lagCount(rows) = stats.GroupCount(loc(rows));
end
Excerpt: step1_prepare_data.m, addHistoryFeatures() · Feature engineering · 12 / 20
Notes: Here’s the core of the implementation. findgroups turns the five fixed attributes into a numeric building ID. Then, for each year, we keep only the building-year averages from earlier years, find each building’s most recent record and its overall statistics, and write the four lag features into the rows for that year. Because the filter is strictly earlier years, year 6 validation only sees years 1 to 5, and the test year sees years 1 to 6. The whole function is vectorised with groupsummary and ismember, so it runs in seconds.

## Slide 13: Missing values get their own branch in tree models
3 · IMPLEMENTATION
Without surrogate splits, a MATLAB regression tree stops an observation with a missing value at the split node. With about 1 in 3 Energy Star ratings missing, this blurred many predictions.
function X = fillSentinel(X)
% Replace NaN in numeric predictors with an out-of-range value for tree models.
isNum = varfun(@isnumeric, X, "OutputFormat", "uniform");
for v = string(X.Properties.VariableNames(isNum))
X.(v) = fillmissing(X.(v), "constant", -999);
end
end
Applied to tree models only. Linear regression uses training-median imputation.
Code: fillSentinel.m · Feature engineering · 13 / 20
Notes: One technical detail made a real difference. By default, MATLAB regression trees don’t use surrogate splits, so when a building has a missing value at a split, it stops at that node and gets a rough average instead of a proper prediction. A third of buildings have no Energy Star rating, so this affected a lot of rows. Our fix replaces missing numbers with minus 999, a value far outside every real range, so the tree can learn a separate branch for missing data. The missing-rating flag keeps that information explicit. Linear regression can’t use a sentinel like this, so it uses median imputation from the training years.

## Slide 14: All candidates are Regression Learner models
4 · MODELS
Regression Learner model | MATLAB function | Settings
Mean (baseline) | — | Predicts the training average
Linear Regression | fitlm | Median imputation for gaps
Fine / Medium Tree | fitrtree | Min leaf size 4 / 12
Bagged Trees | fitrensemble, Bag | 100 trees, leaf 5, 1/3 of predictors per split
Boosted Trees | fitrensemble, LSBoost | Rate 0.1, 63 splits, leaf 20, 300 trees, 70% of predictors
Boosted Trees, tuned | fitrensemble, LSBoost | 4-setting grid; tree count picked on validation
Neural Network | fitrnet | 1 hidden layer of 10, standardised inputs
Code: step2_train_models.m, compare_app_models.m · Models and results · 14 / 20
Notes: Every model we used is available in MATLAB’s Regression Learner app, which keeps the solution easy to reproduce. We start with two baselines: predicting the training mean, and linear regression. Then single regression trees, Bagged Trees, which is a random forest because each split only sees a third of the predictors, and Boosted Trees using least-squares boosting. We tuned the boosted model on a small grid and picked the number of trees from the validation curve. We also tried a small neural network. All are trained in code with fitlm, fitrtree, fitrensemble and fitrnet so the whole comparison runs from one script.

## Slide 15: Without building history, the best test-like RMSE was 46.84
4 · RESULTS, ITERATION 1
Model | RMSE, all of year 6 | RMSE, test-like
Mean (baseline) | 57.21 | 64.88
Linear Regression | 50.54 | 54.26
Boosted Trees, log target | 45.30 | 49.94
Boosted Trees | 44.68 | 48.82
Boosted Trees, tuned | 44.68 | 48.51
Bagged Trees | 42.83 | 47.02
Average of Bagged and Boosted | 42.95 | 46.84
62 predictors, no history features, missing values left as NaN. The log target did not help.
Validation: train years 1–5, score year 6 · Models and results · 15 / 20
Notes: This was our first full iteration, with 62 predictors and no history features. Each step helped: linear regression beat the mean by about 10 points, and tree ensembles beat linear regression by another 7. The log-transformed target scored slightly worse, so we kept the raw target. Bagged Trees was the best single model at 47.02, and averaging it with tuned Boosted Trees edged it down to 46.84. Notice the test-like column is consistently about 4 points worse than the all-states column, which is exactly why we choose models on the test-like score.

## Slide 16: History features cut test-like error by about 45%
4 · RESULTS, ITERATION 2
Model | All of year 6 | Test-like | Iteration 1 | Change
Mean (baseline) | 57.21 | 64.88 | 64.88 | —
Neural Network | 47.80 | 50.60 | — | —
Linear Regression | 36.10 | 35.83 | 54.26 | −34%
Fine Tree | 37.65 | 31.01 | — | —
Medium Tree | 36.72 | 28.79 | — | —
Boosted Trees | 36.92 | 27.15 | 48.82 | −44%
Bagged Trees | 31.42 | 26.35 | 47.02 | −44%
Boosted Trees, tuned | 33.60 | 26.35 | 48.51 | −46%
Average of Bagged and Boosted (final) | 31.92 | 25.99 | 46.84 | −45%
66 predictors with history features and missing-value fix · Models and results · 16 / 20
Notes: Here’s the second iteration, with the four history features and the missing-value fix. Every model improved dramatically. Even linear regression dropped from 54 to under 36. The tree ensembles fell by about 44 to 46 percent. Our final model, the average of Bagged Trees and tuned Boosted Trees, reaches 25.99 on the test-like data, against 46.84 before. The small neural network did poorly at 50.6; it would need much more tuning. One interesting change: the test-like score is now better than the all-states score, and since the test set has no State 6, the test-like column is the one that counts.

## Slide 17: With history, boosting peaks after about 40 trees
4 · TUNING
Max splits | Min leaf | Best trees | Test-like RMSE
127 | 10 | 38 | 26.16
127 | 30 | 42 | 26.17
255 | 10 | 32 | 26.25
255 | 30 | 38 | 26.30
Learning rate 0.1 throughout; up to 500 trees, best count read from the validation curve.
Iteration 1 needed 496 trees to reach 48.51.
All four settings land within 0.14 of each other: the model is not sensitive to these choices.
Code: step2_train_models.m, tuning grid · Models and results · 17 / 20
Notes: For the boosted model we ran a small grid: two tree depths and two leaf sizes at a learning rate of 0.1, each with up to 500 trees, reading the best number of trees off the validation curve. All four settings finished within 0.14 RMSE of each other, so the model isn’t sensitive to these choices. The striking change is the tree count. Without history, boosting needed nearly 500 trees to reach 48.5. With history it peaks after about 40, because the history features already carry most of the signal. When the chosen setting was refit with 38 trees, it scored 26.35, slightly above the grid’s 26.16, because each split samples predictors at random.

## Slide 18: A building’s history and type drive the prediction
4 · INTERPRETATION
Boosted Trees | Importance
lag_last | 42%
facility_type | 19%
lag_mean | 16%
energy_star_rating | 10%
lag_gap | 2%
lag_count | 2%
floor_area | 1%
year_built | 1%
Bagged Trees | Importance
lag_last | 27%
lag_mean | 21%
facility_type | 18%
energy_star_rating | 10%
log_floor_area | 4%
floor_area | 4%
year_built | 4%
lag_gap | 1%
History features account for 62% (boosted) and 49% (bagged) of importance. No weather variable makes either top 8.
predictorImportance on final models retrained on years 1–6 · Models and results · 18 / 20
Notes: To understand the models, we looked at predictor importance in the final models trained on all six years. Both agree on the top four: the building’s last known energy use, its average past use, its facility type and its Energy Star rating. The four history features together account for 62 percent of the boosted model’s importance and 49 percent of the bagged model’s. No weather variable makes the top eight of either model. In plain terms, the best predictor of a building’s energy use this year is its energy use last year, adjusted for what kind of building it is.

## Slide 19: The final submission and how to reproduce it
5 · SUBMISSION
Item | Value
Final model | Average of Bagged and tuned Boosted Trees
Training data | All 75,757 rows, years 1–6
Predictions | 9,705, ids match sample file
Prediction mean / median | 72.4 / 61.2
Invalid values | 0 (asserted in code)
Test-like validation RMSE | 25.99
>> runAll
step1_prepare_data
step2_train_models
step3_make_submission
Fixed seeds with rng(0). Runs end to end in about 15–25 minutes.
github.com/dgmtriet/Hackathon2026 · branch lam_workings · Submission and conclusions · 19 / 20
Notes: For the submission, the chosen approach, the average of Bagged Trees and tuned Boosted Trees, is retrained on all 75,757 rows from years 1 to 6, since year 6 is the most recent and most relevant data. It produces 9,705 predictions in the same id order as the sample file, with a mean of 72.4 and median of 61.2. The script asserts that the order matches and that every value is valid before writing the file. Everything runs from a single command, runAll, with fixed random seeds, in about 15 to 25 minutes. The code and README are public on GitHub.

## Slide 20: From 64.88 to 25.99 RMSE, a 60% reduction
5 · CONCLUSIONS
WHAT WE LEARNED
Audit how the test set differs before choosing a split
Domain insight beat model choice: history cut error by 45%
Know how your tools treat missing values
Standard Regression Learner models were enough
LIMITATIONS AND NEXT STEPS
6.6% of test buildings have no history
Validation is one year; true test score unknown
Next: flag buildings far above prediction for retrofits
Next: tune the neural network; add group averages
Thank you · Submission and conclusions · 20 / 20
Notes: To conclude: we went from 64.88 RMSE for a naive baseline to 25.99, a 60 percent reduction. Four lessons stand out. Audit the test set before choosing a validation split. Domain insight mattered more than the model: recognising that buildings repeat over the years cut our error by 45 percent. Know how your tools treat missing values. And standard Regression Learner models were enough when used carefully. There are limitations: 6.6 percent of test buildings have no history, so they get weaker predictions, and our validation covers a single year, so the true test score may differ. Next, we’d use the model as intended, flagging buildings that use far more energy than predicted as retrofit candidates. Thank you.